## Slide 1
First Light and Science with the Near-Infrared Planet Searcher (NIRPS) Romain Allart on behalf of the NIRPS consortium
Trottier postdoctoral fellow
Université de Montréal, Institut Trottier de Recherche sur les Exoplanètes
http://www.astro.umontreal.ca/nirps
https://www.eso.org/sci/facilities/develop/instruments/NIRPS.html

## Slide 2
Co-PIs : R. Doyon (UdeM) + F. Bouchy (Geneva)
Co-Is : F. Pepe, N. Santos, R. Rebolo, X. Delfosse,
J. De Medeiros, G. Wade
Proj. Scientist : E. Artigau (UdeM)
Proj. Manager : L. Malo/F. Baron (UdeM)
System Engineer : F. Wildi (Geneva)

## Slide 3
Top Level Requirements
Y, J, H bands simultaneously
Fiber feed from AO
Two observing modes:
  HA: R~84’000
  HE: R~72’000
High RV precision (1 m/s)
and high spectral fidelity
Simultaneous operation with HARPS
DRS: Espresso-like + APERO (SPIRou)
Milestones
Proposals ( ) 2014/2015
Kickoff Jan 2016
FDR May 2017
PAE Front End Sept 2019
Front-End Comm Nov 2019
PAE Spectrograph Oct 2021
Front-End + Fiber Comm Dec 2021
AIV in La Silla March-April 2022
First Light June 2022
Science Operations April 2023

## Slide 4
Cryogenic white pupil spectrograph
R4 echelle grating (73x73 mm pupil, 13.3 l/mm)
5 ZnSe prisms train for cross-dispersion
H4RG-15 detector 4k x 4k
Fiber Link
HA mode
R=84’000
HEmode
R=72’000
Sky/Ref
Oct 29 (0.4’’)
Oct 66 (0.9’’)
Science fibers
Rect 33x132 m
Notes: NIRPS in a nutschell
4 main sub-systems

## Slide 5
Front-end with AO system
Fiber Stretcher
Prisms train
Cold Shield and Cryostat
Fiber Double Scrambler
Calibration Unit
Echelle R4 grating

## Slide 6
Double Scrambler
Fiber Stretcher
Cryostat
Fiber Link
Cryo-coolers
NIRPS Room - Coudé Floor of 3.6m
Front-End
ESO 3.6m telescope

## Slide 8
NIRPS first light 17 May 2022
And 4 commissioning later…

## Slide 9
tet01 Mic I=4.73
tet02 Mic J=5.84
Separation 0.3 arcsec
AO loop open
AO loop closed
NIRPS AO imaging capability

## Slide 10
Wavelength solution
UrNe + Fabry-Pérot
accuracy = 0.75 m/s
FP sequence over 1h45 : 6 cm/s RMS
40 cm/s

## Slide 11: Thermal stability
sub-mK thermal stability achieved over several months
1 mK

## Slide 12: Thermal stability
Small coupling of the cryo-optics and room temperature.
  HARPS-like thermal enclosure under construction
Power outage

## Slide 13
Chart: NIRPS throughput in YJH-band - seeing = 0.9"

## Slide 14: Modal noise
A0 scrambling and stretcher reduce modal noise by a factor 5 (HE) and 10 (HA)
Relatively stable over several days.
Can be calibrated out using fast-rotating hot stars (also used for telluric correction)

## Slide 15
CO2
O2
H2O
‘lost order’ from fiber train absorption
Proxima NIRPS spectra
Spectral coverage 971 – 1854 𝝁m (70 spectral orders)
Spectral resolution HA = 84’000 HE = 72’000
Operated simultaneously with HARPS

## Slide 16
NIRPS connected to solar telescope HELIOS
Courtesy : X. Dumusque
to observe the Sun as a star with HARPS and NIRPS every possible day

## Slide 17: Preliminary results - Proxima
No GP
Telluric-corrected RVs extracted
with the line-by-line (LBL) extraction method
Telluric correction
Credit: Etienne Artigau; Allart et al. 2022
uncertainty ~60 cm/s
Uncertainty of our closest competitor
H2O lines
O2 lines
CO2 lines
CH4 lines

## Slide 18: Preliminary results – GJ581
Credit: Etienne Artigau

## Slide 19: Water detection in WASP-127b
Credit: Frédéric Genest

## Slide 20: Abundance determination – LHS1140
Credit: Farbod Jahandar

## Slide 21
NIRPS main science cases
Detection of exoplanets around M dwarfs, active stars and young stars
RV search for planets around M dwarf to image with ELT
Mass and density characterization of transiting exoplanets (mainly from TESS)
Exoplanet atmosphere characterization through transmission spectroscopy at high resolution
Mitigation of stellar activity using chromatic effect + sensitive spectral lines + Zeeman broadening
NIRPS AO guiding camera to identify nearby stellar component and/or rule out blended EBs
Long term monitoring of Sun observed as a star in both visible + nIR
NIRPS GTO: 725 nights over 5 years since April 1st 2023!

## Slide 22: NIRPS GTO Science Highlights
PRV focused on M dwarfs
Time is distributed equally over three work packages
  WP1: blind searches
  WP2: transit follow-up
  WP3: atmospheric characterization
NIRPS GTO: 725 nights over 5 years since April 1st 2023!

## Slide 23: WP1 – RV searches Coordinator: Lucille Mignon & Xavier Delfosse
A census of the planetary system in the Solar Neighbourhood
  Imaging target for the ELT (ANDES currently in PDR)
GAUCHO : Grasping exoplanet Architectures in UltraCool Hosts
PACAMARA: Probing Age-CAlibrated M dwARfs for exoplAnets
…
AD Leo
Carmona et al (2023)
Credit: Etienne Artigau
CRAQ students involved:

## Slide 24: WP2 – Mass characterization of exoplanets transiting M dwarfs Coordinators: F. Bouchy & R. Doyon
Occurence of giant exoplanets around M dwarfs
Density and composition of super-Earth and sub-Neptunes around M dwarfs
The radius valley as a key tracer of planet formation and evolution
Iron core mass fraction of rocky planets
Exploring the diversity of transiting exoplanets within the Habitable Zone
Architechture of multi-planetary systems as a test of planet formation theories
Young planets transiting M dwarf
…
Credit: Charles Cadieux
CRAQ students involved:

## Slide 25: WP3 – Atmospheric characterization Coordinator: Romain Allart
Transmission spectroscopic survey to unveil the origin of the evaporation desert
An emission survey probing the transition between hot and ultra-hot Jupiters.
Elemental and isotopic abundances and detailed chemistry and dynamics with “ELT-quality” NIRPS/HARPS Legacy Transmission Spectra
Characterizing young planets discovered by TESS
Transmission spectroscopy of the TRAPPIST-1 planets
…
CRAQ students involved:

## Slide 26: Summary
HARPS is not alone!
Exciting and very encouraging results from commissioning
The best has yet to come from the NIRPS consortium and the community.